- Static Braking

  - Static Brake shall according to suitable types and range of principle are as below:

    - The same vehicle category symbol.

    - The same axle set type.

    - The same brand and vehicle type series.

    - The chassis vehicle have had same axle set type.

    - The same chassis brand.

    - Chassis manufacturers declared that the same chassis vehicle type series.

  - Stipulation of static braking:

    - Static Brake efficiency

      - Small vehicle and its trailer attached: above 50% vehicle weight.

      - Large vehicle: above 50% vehicle weight.

      - Trailer: above 50% vehicle axle weight.

    - Balance ratio: The brake force variation between two sides of wheel shall not exceed 30%.

    - Parking brake: 16% or above of vehicle weight (not apply to trailer)

    - If the gross vehicle weight of trailer dose not exceeds 400 kg, then it may be without the brake system. From 2010/1/1, if the gross vehicle weight of trailer does not exceeds 750 kg, then it may not be equipped with the brake system.