- The requirement of vehicle tilt stability

  - The requirement of vehicle tilt stability shall according to suitable types and range of principle are as below：

    - The same vehicle category symbol.

    - The same type of vehicle body.

    - The same axle set type.

    - The same brand and vehicle type series.

    - The chassis vehicle have had same axle set type.

    - The same chassis brand.

    - Chassis manufacturers declared that the same chassis vehicle type series.

    - Scaling ladder type firefighting vehicle can be free from this tilt stability test.

  - From 2000/1/1, vehicle height ≧ 3.5 m, its vehicle tilt stability have to comply with this regulation:

    - The tilt stability on both left & right side of vehicle shall be greater than 35 degree, under curb weight condition.

    - For special vehicle, when 1.2 times of curb weight is larger than gross vehicle weight, the inspection standard can be 30 degree.

  - From 2007/01/01, new type of passenger vehicle with vehicle height exceeds 3.4 m and from 2008/01/01, all type of passenger vehicle with height exceeds 3.4m, the tilt stability shall comply with this regulation.

    - The tilt stability on both left and right side of large passenger vehicle shall be greater than 28 degree under the following loading condition.

    - Loading condition

      - The vehicle shall be at its mass in running order: The mass of the driver and, if applicable, of the crew member is assessed at 75 kg, the fuel tank is filled to 90 % and the other liquid containing systems (except those for used water) to 100 % of the capacity specified by the manufacturer.

      - Loads equal to Q shall be placed on each passenger seat. In case of city bus, Q= 68 kg. In case of other classes of large passenger vehicle, Q= 71 kg.

      - The centre of gravity of the loads Q specified in paragraph 8.3.2.2 or 75 kg representing standees, shall be uniformly distributed over the standee area respectively, at a height of 875 mm.

      - Where a vehicle is equipped to carry luggage on the roof, a uniformly distributed mass (BX) of not less than that declared by the manufacturer representing such baggage shall be secured to the roof. BX, declared by the manufacturer, must have a numeric value not less than 75 kg/m2. The other baggage compartments shall not contain any baggage.

      - The front axle load, rear axle load and gross vehicle weight under the above loading condition shall not exceed the respective design value declared by the chassis manufacturer.