- Sound level of audible warning device

  - The effective date of this regulation is from 2001/7/1.

  - Sound level of audible warning device shall according to suitable types and range of principle are as below：

    - The same vehicle category symbol.

    - The same brand and vehicle type series.

    - The same chassis brand.

    - Chassis manufacturers announced that the same chassis vehicle type series.

    - If use chassis vehicle instead of completed vehicle for entire or partial testing, which shall according to suitable types and range of principle are as below：

      - The same brand.

      - Chassis manufacturers declared that the same chassis vehicle type series.

  - Sound level of audible warning device for motor vehicle: At distance 7 m in front of vehicle, 0.5 to1.5m above ground, the sound level shall be within 93 dBA and 112 dBA.

  - Sound level of audible warning device for motorcycle: At distance 7 m in front of vehicle, 0.5 to1.5m above ground, the sound level shall be within 80 dBA and 112 dBA.