- Installation requirements of pay load meter

  - Payload meter: device installed on the sandstone-carrying vehicle, used to indicate the loading weight therein.

  - The heavy dump truck or semi-trailer above 20 tons, loading gravel and sand or soil, shall comply with this regulation from 2001/7/1 and shall use the payload meter approved by these regulations.

  - Installation requirements of pay load meter shall according to suitable types and range of principle are as below：

    - The same vehicle category symbol.

    - The same axle set type.

    - The same brand and vehicle type series.

    - The chassis vehicle have had same axle set type.

    - The same chassis brand.

    - Chassis manufacturers declared that the same chassis vehicle type series.

  - Inspection standard: Installing position, payload indicating and measuring tolerance of payload, shall comply with requirements specified below in this regulation.

    - Installing position: The display device of payload scale meter shall be installed on the right side of vehicle that can be observed directly.

    - Maximum scale of measuring: The largest measuring scale shall be the approved volume of heavy truck or trailer times 1.5, the specific weight, then within the range of the value times 1.2 to 2 .

    - The measuring tolerance uses the approved MT counted by the nearest integer larger than the approved weight as the simulated load. The plus/minus error of reading value of the pay load meter, under the simulating load condition, shall not exceed 5% of the actual pay load value.