- The thermal-insulation protection device of exhaust system for motorcycle

  - The thermal-insulation protection device of exhaust system for motorcycle shall according to suitable types and range of principle are as below：

    - The same vehicle category symbol.

    - The same brand and vehicle type series.

  - The thermal-insulation protection device of exhaust system for motorcycle: From 2002/1/1, the temperature of the surface geometric center, the point 3-cm (0.5 cm of allowable range) distance from the end-edge on the front/rear horizontal level relative to the silencer and fixing point of the device (if constructed with indentation shape, take the nearest available point) shall conform to the following requirement specified:

    - For steel material: the measured temperature shall not exceed 60℃.

    - For resin material: the measured temperature shall not exceed 70℃.

  - This test may be exempted if the passenger or the pedestrians will not contact the exhaust system of motorcycle while normal operating or parking condition of the motorcycle.