- Tyre

Refer to: R30 02-S14, R54 00-R2/C1

  - Effective date and Scope:

    - Effective date from 2006/7/1, the new tyres of category symbols M, N and O, and from 2008/7/1 all tyres variants of category symbols M, N and O, shall comply with this regulation.

    - As for the category symbol N1, the new pneumatic tyres shall comply with paragraphs either 28.4. or 28.5. specified below in this regulation.

    - The applicants applying for low volume safety approval could exempt from regulation of “tyre” except large passenger vehicle and child-only vehicle.

    - Applying for vehicle-by-vehicle low volume safety approval, the vehicle could exempt from regulation of “tyre”.

  - Definitions:

    - Snow tyre: means a tyre whose tread pattern and whose structure are primarily designed to ensure in mud and fresh or melting snow a performance better than that of an ordinary (road-type) tyre. The tread pattern of a snow tyre generally consists of groove (rib) and/or solid-block elements more widely spaced than on an ordinary (road type) tyre;

    - "Diagonal" or "bias-ply": describes a pneumatic-tyre structure in which the ply cords extend to the beads and are laid at alternate angles of substantially less than 90 degrees to the centre line of the tread;

    - Bias-belted: describes a pneumatic-tyre structure of diagonal (bias-ply) type in which the carcass is restricted by a belt comprising two or more layers of substantially inextensible cord material laid at alternate angles close to those of the carcass;

    - "Radial" describes a pneumatic-tyre structure in which the ply cords extend to the beads and are laid substantially at 90 degrees to the centre line of the tread, the carcass being stabilized by an essentially inextensible circumferential belt;

    - Reinforced or Extra Load: describes a pneumatic-tyre structure in which the carcass is more resistant than that of the corresponding standard tyre;

    - "Temporary use spare tyre" means a tyre different from a tyre intended to be fitted to any vehicle for normal driving conditions but intended only for temporary use under restricted driving conditions;

    - T-type temporary use spare tyre: means a type of temporary use spare tyre designed for use at inflation pressures higher than those established for standard and reinforced tyres;

    - Cord: means the strands forming the fabric of the plies in the pneumatic tyre;

    - Ply: means a layer of rubber-coated parallel cords;

    - Carcass: means that part of a pneumatic tyre other than the tread and the rubber side walls which, when inflated, bears the load;

    - Tread: means that part of a pneumatic tyre which comes into contact with the ground, protects the carcass against mechanical damage and contributes to ground adhesion;

    - Section width: means the linear distance between the outsides of the side walls of an inflated pneumatic tyre, excluding elevations due to labelling (marking), decoration or protective bands or ribs;

    - Overall width: means the linear distance between the outsides of the side walls of an inflated pneumatic tyre, including labelling (marking), decoration and protective bands or ribs;

    - Section height: means a distance equal to half the difference between the outer diameter of the tyre and the nominal rim diameter;

    - Nominal aspect ratio (Ra): means the centuple of the number obtained by dividing the number expressing the section height by the number expressing the nominal section width;

    - Outer diameter: means the overall diameter of an inflated new pneumatic tyre;

    - Rim: means the support for a tyre-and-tube assembly, or for a tubeless tyre, on which the tyre beads are seated;

    - Nominal rim diameter: means the diameter of the rim on which a tyre is designed to be mounted; The values of the "d" symbols expressed in millimetres are shown below:

| Nominal rim diameter code ("d" symbol) | Value of the "d" symbol expressed in mm | Nominal rim diameter code ("d" symbol) | Value of the "d" symbol expressed in mm | Nominal rim diameter code ("d" symbol) | Value of the "d" symbol expressed in mm | Nominal rim diameter code ("d" symbol) | Value of the "d" symbol expressed in mm |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 8 | 203 | 16 | 406 | 24 | 610 | 24.5 | 622 |
| 9 | 229 | 17 | 432 | 25 | 635 | 26 | 660 |
| 10 | 254 | 18 | 457 | 14.5 | 368 | 28 | 711 |
| 11 | 279 | 19 | 482 | 16.5 | 419 | 30 | 762 |
| 12 | 305 | 20 | 508 | 17.5 | 445 |  |  |
| 13 | 330 | 21 | 533 | 19.5 | 495 |  |  |
| 14 | 356 | 22 | 559 | 20.5 | 521 |  |  |
| 15 | 381 | 23 | 584 | 22.5 | 572 |  |  |

    - Speed category: means the maximum speed which the tyre can sustain, expressed by speed category symbol (see table below).

| Speed-category symbol | Maximum speed (km/h) | Speed-category symbol | Maximum speed (km/h) |
| --- | --- | --- | --- |
| F | 80 | R | 170 |
| G | 90 | S | 180 |
| J | 100 | T | 190 |
| K | 110 | U | 200 |
| L | 120 | H | 210 |
| M | 130 | V | 240 |
| N | 140 | W or Z | 270 |
| P | 150 | Y or Z | 300 |
| Q | 160 |  |  |

    - Theoretical rim： means the theoretical rim whose width would be equal to x times the nominal section width of a tyre. The value of x shall be specified by the manufacturer of that tyre;

    - Load capacity index: means a number associated to the reference mass a tyre can carry when operated in conformity with requirements governing utilization specified by the manufacturer. A=Load-capacity index, B=Corresponding mass of the vehicle which is to be carried.

| A | B | A | B | A | B | A | B | A | B |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 45 | 41 | 145 | 82 | 475 | 123 | 1550 | 164 | 5000 |
| 1 | 46.2 | 42 | 150 | 83 | 487 | 124 | 1600 | 165 | 5150 |
| 2 | 47.5 | 43 | 155 | 84 | 500 | 125 | 1650 | 166 | 5300 |
| 3 | 48.7 | 44 | 160 | 85 | 515 | 126 | 1700 | 167 | 5450 |
| 4 | 50 | 45 | 165 | 86 | 530 | 127 | 1750 | 168 | 5600 |
| 5 | 51.5 | 46 | 170 | 87 | 545 | 128 | 1800 | 169 | 5800 |
| 6 | 53 | 47 | 175 | 88 | 560 | 129 | 1850 | 170 | 6000 |
| 7 | 54.5 | 48 | 180 | 89 | 580 | 130 | 1900 | 171 | 6150 |
| 8 | 56 | 49 | 185 | 90 | 600 | 131 | 1950 | 172 | 6300 |
| 9 | 58 | 50 | 190 | 91 | 615 | 132 | 2000 | 173 | 6500 |
| 10 | 60 | 51 | 195 | 92 | 630 | 133 | 2060 | 174 | 6700 |
| 11 | 61.5 | 52 | 200 | 93 | 650 | 134 | 2120 | 175 | 6900 |
| 12 | 63 | 53 | 206 | 94 | 670 | 135 | 2180 | 176 | 7100 |
| 13 | 65 | 54 | 212 | 95 | 690 | 136 | 2240 | 177 | 7300 |
| 14 | 67 | 55 | 218 | 96 | 710 | 137 | 2300 | 178 | 7500 |
| 15 | 69 | 56 | 224 | 97 | 730 | 138 | 2360 | 179 | 7750 |
| 16 | 71 | 57 | 230 | 98 | 750 | 139 | 2430 | 180 | 8000 |
| 17 | 73 | 58 | 236 | 99 | 775 | 140 | 2500 | 181 | 8250 |
| 18 | 75 | 59 | 243 | 100 | 800 | 141 | 2575 | 182 | 8500 |
| 19 | 77.5 | 60 | 250 | 101 | 825 | 142 | 2650 | 183 | 8750 |
| 20 | 80 | 61 | 257 | 102 | 850 | 143 | 2725 | 184 | 9000 |
| 21 | 82.5 | 62 | 265 | 103 | 875 | 144 | 2800 | 185 | 9250 |
| 22 | 85 | 63 | 272 | 104 | 900 | 145 | 2900 | 186 | 9500 |
| 23 | 87.5 | 64 | 280 | 105 | 925 | 146 | 3000 | 187 | 9750 |
| 24 | 90 | 65 | 290 | 106 | 950 | 147 | 3075 | 188 | 10000 |
| 25 | 92.5 | 66 | 300 | 107 | 975 | 148 | 3150 | 189 | 10300 |
| 26 | 95 | 67 | 307 | 108 | 1000 | 149 | 3250 | 190 | 10600 |
| 27 | 97 | 68 | 315 | 109 | 1030 | 150 | 3350 | 191 | 10900 |
| 28 | 100 | 69 | 325 | 110 | 1060 | 151 | 3450 | 192 | 11200 |
| 29 | 103 | 70 | 335 | 111 | 1090 | 152 | 3550 | 193 | 11500 |
| 30 | 106 | 71 | 345 | 112 | 1120 | 153 | 3650 | 194 | 11800 |
| 31 | 109 | 72 | 355 | 113 | 1150 | 154 | 3750 | 195 | 12150 |
| 32 | 112 | 73 | 365 | 114 | 1180 | 155 | 3875 | 196 | 12500 |
| 33 | 115 | 74 | 375 | 115 | 1215 | 156 | 4000 | 197 | 12850 |
| 34 | 118 | 75 | 387 | 116 | 1250 | 157 | 4125 | 198 | 13200 |
| 35 | 121 | 76 | 400 | 117 | 1285 | 158 | 4250 | 199 | 13600 |
| 36 | 125 | 77 | 412 | 118 | 1320 | 159 | 4375 | 200 | 14000 |
| 37 | 128 | 78 | 425 | 119 | 1360 | 160 | 4500 |  |  |
| 38 | 132 | 79 | 437 | 120 | 1400 | 161 | 4625 |  |  |
| 39 | 136 | 80 | 450 | 121 | 1450 | 162 | 4750 |  |  |
| 40 | 140 | 81 | 462 | 122 | 1500 | 163 | 4875 |  |  |

  - Tyre shall according to suitable types and range of principle are as below：

    - Brand

    - Nominal aspect ratio

    - Category of use (ordinary (road-type) or snow tyre or for temporary use)

    - Structure (diagonal (bias-ply), bias-belted, radial-ply)

    - The suitable of vehicle’s category.

  - New pneumatic tyres designed primarily, but not only, for vehicles in category symbols M1 ,N1, O1 and O2.

    - General Specifications:

      - Tyre-size designation is a designation showing:

        - The nominal section width (mm) (This width must be expressed in mm, except in the case of the types of tyre for which the size designation is shown in the first column of the tables)

          - Tyres in Diagonal Construction (European tyres)

| Size | Measuring rim width code | Overall diameter (mm) | Tyre section width (mm) | Nominal rim diameter “d” (mm) |
| --- | --- | --- | --- | --- |
| Super Ballon Series |  |  |  |  |
| 4.80-10 5.20-10 5.20-12 5.60-13 5.90-13 6.40-13 5.20-14 5.60-14 5.90-14 6.40-14 5.60-15 5.90-15 6.40-15 6.70-15 7.10-15 7.60-15 8.20-15 | 3.5 3.5 3.5 4 4 4.5 3.5 4 4 4.5 4 4 4.5 4.5 5 5.5 6 | 490 508 558 600 616 642 612 626 642 666 650 668 692 710 724 742 760 | 128 132 132 145 150 163 132 145 150 163 145 150 163 170 180 193 213 | 254 254 305 330 330 330 356 356 356 356 381 381 381 381 381 381 381 |
| Low Section Series |  |  |  |  |
| 5.50-12 6.00-12 7.00-13 7.00-14 7.50-14 8.00-14 6.00-15L | 4 4.5 5 5 5.5 6 4.5 | 552 574 644 668 688 702 650 | 142 156 178 178 190 203 156 | 305 305 330 356 356 356 381 |
| Super Low Section Series註 |  |  |  |  |
| 155-13/6.15-13 165-13/6.45-13 175-13/6.95-13 155-14/6.15-14 165-14/6.45-14 175-14/6.95-14 185-14/7.35-14 195-14/7.75-14 | 4.5 4.5 5 4.5 4.5 5 5.5 5.5 | 582 600 610 608 626 638 654 670 | 157 167 178 157 167 178 188 198 | 330 330 330 356 356 356 356 356 |
| Ultra Low Section |  |  |  |  |
| 5.9-10 6.5-13 6.9-13 7.3-13 | 4 4.5 4.5 5 | 483 586 600 614 | 148 166 172 184 | 254 330 330 330 |

Note: The following size designations are accepted: 185-14/7.35-14 or 185-14 or 7.35-14 or 7.35-14/185-14.

          - Millimetric Series - Radial (European tyres)

| Size | Measuring rim width code | Overall diameter (mm) | Tyre section width (mm) | Nominal rim diameter “d” (mm) |
| --- | --- | --- | --- | --- |
| 125 R 10 | 3.5 | 459 | 127 | 254 |
| 145 R 10 | 4 | 492 | 147 | 254 |
| 125 R 12 | 3.5 | 510 | 127 | 305 |
| 135 R 12 | 4 | 522 | 137 | 305 |
| 145 R 12 | 4 | 542 | 147 | 305 |
| 155 R 12 | 4.5 | 550 | 157 | 305 |
| 125 R 13 | 3.5 | 536 | 127 | 330 |
| 135 R 13 | 4 | 548 | 137 | 330 |
| 145 R 13 | 4 | 566 | 147 | 330 |
| 155 R 13 | 4.5 | 578 | 157 | 330 |
| 165 R 13 | 4.5 | 596 | 167 | 330 |
| 175 R 13 | 5 | 608 | 178 | 330 |
| 185 R 13 | 5.5 | 624 | 188 | 330 |
| 125 R 14 | 3.5 | 562 | 127 | 356 |
| 135 R 14 | 4 | 574 | 137 | 356 |
| 145 R 14 | 4 | 590 | 147 | 356 |
| 155 R 14 | 4.5 | 604 | 157 | 356 |
| 165 R 14 | 4.5 | 622 | 167 | 356 |
| 175 R 14 | 5 | 634 | 178 | 356 |
| 185 R 14 | 5.5 | 650 | 188 | 356 |
| 195 R 14 | 5.5 | 666 | 198 | 356 |
| 205 R 14 | 6 | 686 | 208 | 356 |
| 215 R 14 | 6 | 700 | 218 | 356 |
| 225 R 14 | 6.5 | 714 | 228 | 356 |
| 125 R 15 | 3.5 | 588 | 127 | 381 |
| 135 R 15 | 4 | 600 | 137 | 381 |
| 145 R 15 | 4 | 616 | 147 | 381 |
| 155 R 15 | 4.5 | 630 | 157 | 381 |
| 165 R 15 | 4.5 | 646 | 167 | 381 |
| 175 R 15 | 5 | 660 | 178 | 381 |
| 185 R 15 | 5.5 | 674 | 188 | 381 |
| 195 R 15 | 5.5 | 690 | 198 | 381 |
| 205 R 15 | 6 | 710 | 208 | 381 |
| 215 R 15 | 6 | 724 | 218 | 381 |
| 225 R 15 | 6.5 | 738 | 228 | 381 |
| 235 R 15 | 6.5 | 752 | 238 | 381 |
| 175 R 16 | 5 | 686 | 178 | 406 |
| 185 R 16 | 5.5 | 698 | 188 | 406 |
| 205 R 16 | 6 | 736 | 208 | 406 |

          - 45 Series - Radial on TR Metric 5 degrees Rims

| Size | Measuring rim width code | Overall diameter (mm) | Tyre section width (mm) |
| --- | --- | --- | --- |
| 280/45 R 415 | 240 | 661 | 281 |

        - A conventional number denoting the nominal rim diameter and corresponding to its diameter expressed either by codes (numbers below 100) or in millimetres (numbers above 100)

        - The indication of the structure

      - It does not apply to tyres designed for the equipment of vintage cars and competitions.

    - Test Procedure

      - Load/speed performance test

        - Where application is made for tyres identified by means of letter code "ZR" within the size designation and suitable for speeds over 300 km/h, the above load/speed test is carried out on one tyre at the load and speed conditions marked on the tyre.

        - Preparing the tyre

          - Mount a new tyre on the standard test rim

          - Inflate it to the appropriate pressure as given (in bar) in the table below:

| Speed Category | Diagonal (bias-ply) tyres | Radial tyres | Bias-belted tyres |
| --- | --- | --- | --- |
|  | Ply rating | Standard | Reinforced | Standard |
|  | 4 | 6 | 8 |  |  |  |
| L,M,N P,Q,R,S T,U,H V W Y | 2.3 2.6 2.8 3.0 - - | 2.7 3.0 3.2 3.4 - - | 3.0 3.3 3.5 3.7 - - | 2.4 2.6 2.8 3.0 3.2 3.2 | 2.8 3.0 3.2 3.4 3.6 3.6 | - 2.6 2.8 - - - |

          - T-type temporary use spare tyres: to 4.2 bar.

          - The manufacturer may request, giving reasons, the use of a test-inflation pressure differing from those given above. In such a case the tyre shall be inflated to that pressure.

          - Condition the tyre-and-wheel assembly at test-room temperature for not less than three hours.

          - Readjust the tyre pressure to that specified in 28.4.2.1.2.2~28.4.2.1.2.4 above.

        - Carrying out the test

          - Mount the tyre-and-wheel assembly on a test axle and press it against the outer face of a smooth wheel 1.70m +/- 1% or 2m +/- 1% in diameter.

          - Apply to the test axle a load:

            - Equal to 80% of the maximum load rating equated to the Load Capacity Index for tyres with Speed Symbols L to H inclusive,

            - Equal to 73% of the maximum load rating associated with a maximum speed of 240km/h for tyres Speed Symbol "V"

            - Equal to 68% of the maximum load rating associated with a maximum speed of 270km/h for tyres with speed symbol "W" or “Y”.

        - Throughout the test the tyre pressure must not be adjusted and the test load must be kept constant.

        - During the test the temperature in the test-room must be maintained at between 20 degrees and 30 degrees or at a higher temperature if the manufacturer agrees.

        - Carry the test through, without interruption in conformity with the following particulars:

          - Time taken to pass from zero speed to initial test speed: 10 minutes;

          - Initial test speed: prescribed maximum speed for the type of tyre, less 40km/h in the case of the smooth wheel having 1.70m +/- 1% in diameter or less 30 km/h in the case of the smooth wheel having 2m +/- 1% in diameter;

          - Successive speed increments: 10km/h to the highest testing speed.

          - Duration of test at each speed step except the last: 10 minutes;

          - Duration of test at last speed step: 20 minutes;

          - Maximum test speed: prescribed maximum speed for the type of tyre, less 10km/h in the case of the smooth wheel having 1.7m +/- 1% in diameter or equal to the prescribed maximum speed in the case of the smooth wheel having 2m +/- 1% in diameter.

          - However, for tyres suitable for maximum speed of 300km/h, the duration of test is 20 minutes at the initial test speed step and 10 minutes at the last speed step.

        - If a method other than that described in paragraph 28.3.2.1.3 above is used, its equivalence must be demonstrated.

    - Requirements

      - Load/speed performance test

        - A tyre which after undergoing the load/speed test does not exhibit any tread separation, ply separation, cord separation, chunking or broken cords shall be deemed to have passed the test.

        - However, a tyre marked with the speed symbol "Y" which, after undergoing the relevant test, exhibits superficial blistering of the tyre tread caused by the specific test equipment and conditions, is deemed to have passed the test.

        - The outer diameter of the tyre, measured six hours after the load/speed performance test, must not differ by more than +/-3.5% from the outer diameter as measured before the test.

  - New pneumatic tyres designed primarily, but not only, for vehicles in category symbols M2, M3, N, O3 and O4.

    - it does not apply to tyre types identified by speed category symbols corresponding to speeds below 80 km/h.

    - General Specifications:Tyre-size designation means a designation showing:

      - the nominal section width (mm) (This width must be expressed in mm, except in the case of the types of tyre for which the size designation is shown in the first column of the tables)

        - Code designated sezes mounted on 5 degrees tapered rims or flat base rims-Radial and diagonal constructions

| Tyre size designation | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm) | Section width S (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Radial | Diagonal | Radial | Diagonal |
| Std. Series 4.00R8＊ 4.00R10＊ 4.00R12＊ 4.50R8＊ 4.50R10＊ 4.50R12＊ 5.00R8＊ 5.00R10＊ 5.00R12＊ 6.00R9 6.00R14C 6.00R16＊ 6.50R10 6.50R14C 6.50R16＊ 6.50R20＊ 7.00R12 7.00R14C 7.00R15＊ 7.00R16C 7.00R16 7.00R20 7.50R10 7.50R14C 7.50R15＊ 7.50R16＊ 7.50R17＊ 7.50R20 8.25R15 8.25R16 8.25R17 8.25R20 9.00R15 9.00R16＊ 9.00R20 10.00R15 10.00R20 10.00R22 11.00R16 11.00R20 11.00R22 11.00R24 12.00R20 12.00R22 12.00R24 13.00R20 14.00R20 14.00R24 16.00R20 80 Series 12/80 R 20 13/80 R 20 14/80 R 20 14/80 R 24 14.75/80 R 20 15.5/80 R 20 | 2.50 3.00 3.00 3.50 3.50 3.50 3.00 3.50 3.50 4.00 4.50 4.50 5.00 5.00 4.50 5.00 5.00 5.00 5.00 5.50 5.50 5.50 5.50 5.50 6.00 6.00 6.00 6.00 6.50 6.50 6.50 6.50 6.00 6.50 7.00 7.50 7.50 7.50 6.50 8.00 8.00 8.00 8.50 8.50 8.50 9.00 10.00 10.00 13.00 8.50 9.00 10.00 10.00 10.00 10.00 | 203 254 305 203 254 305 203 254 305 229 356 406 254 356 406 508 305 356 381 406 406 508 254 356 381 406 432 508 381 406 432 508 381 406 508 381 508 559 406 508 559 610 508 559 610 508 508 610 508 508 508 508 610 508 508 | 414 466 517 439 490 545 467 516 568 540 626 728 588 640 742 860 672 650 746 778 784 892 645 686 772 802 852 928 836 860 886 962 840 912 1018 918 1052 1102 980 1082 1132 1182 1122 1174 1226 1176 1238 1340 1370 1008 1048 1090 1192 1124 1158 | 414 466 517 439 490 545 467 516 568 540 625 730 588 650 748 - 672 668 752 778 774 898 645 692 772 806 852 928 836 860 895 970 840 900 1012 918 1050 1102 952 1080 1130 1180 1120 1174 1220 1170 1238 1340 1370 - - - - - - | 107 108 108 125 125 125 132 134 134 160 158 170 177 170 176 181 192 180 197 198 198 198 207 195 212 210 210 210 230 230 230 230 249 246 258 275 275 275 279 286 286 286 313 313 313 336 370 370 446 305 326 350 350 370 384 | 107 108 108 125 125 128 132 134 137 160 158 170 177 172 176 - 192 182 198 198 198 198 207 192 212 210 210 213 234 234 234 234 249 252 256 275 275 275 272 291 291 291 312 312 312 342 375 375 446 - - - - - - |
| Wide base tyre for multipurpose trucks |
| 7.50 R 18 MPT 10.5 R 18 MPT 10.5 R 20 MPT 12.5 R 18 MPT 12.5 R 20 MPT 14.5 R 20 MPT 14.5 R 24 MPT | 5.50 9 9 11 11 11 11 | 457 457 508 457 508 508 610 | 885 905 955 990 1040 1095 1195 | 276 276 330 330 362 362 | 208 270 270 325 325 355 355 |

Note:  (+) Tyres in diagonal construction are identified by an hyphen in place of the letter 'R' (e.g. 5.00-8).

(*) The tyre size designation may be supplemented with the letter 'C' (e.g. 6.00-16C).

        - Code designated sizes mounted on 15 degrees tapered rims-Radial

| Tyre size designation | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm) | Section width S (mm) |
| --- | --- | --- | --- | --- |
| 7 R 17.5＊ 7 R 19.5 8 R 17.5＊ 8 R 19.5 8 R 22.5 8.5 R 17.5 9 R 17.5 9 R 19.5 9 R 22.5 9.5 R 17.5 9.5 R 19.5 10 R 17.5 10 R 19.5 10 R 22.5 11 R 22.5 11 R 24.5 12 R 22.5 13 R 22.5 15 R 19.5 15 R 22.5 16.5 R 19.5 16.5 R 22.5 18 R 19.5 18 R 22.5 70 Series 10/70 R 22.5 11/70 R 22.5 12/70 R 22.5 13/70 R 22.5 | 5.25 5.25 6.00 6.00 6.00 6.00 6.75 6.75 6.75 6.75 6.75 7.50 7.50 7.50 8.25 8.25 9.00 9.75 11.75 11.75 13.00 13.00 14.00 14.00 7.50 8.25 9.00 9.75 | 445 495 445 495 572 445 445 495 572 445 495 445 495 572 572 622 572 572 495 572 495 572 495 572 572 572 572 572 | 752 800 784 856 936 802 820 894 970 842 916 858 936 1020 1050 1100 1084 1124 998 1074 1046 1122 1082 1158 928 962 1000 1033 | 185 185 208 208 208 215 230 230 230 240 240 254 254 254 279 279 300 320 387 387 425 425 457 457 254 279 305 330 |

Note: (*)The tyre size designation may be supplemented with the letter 'C' (e.g. 7 R 17.5C).

        - Tyres For light commercial vehicles-Radial and diagonal constructions

| Tyre size designation | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm) | Section width S (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Radial | Diagonal | Radial | Diagonal |
| Metric designated |
| 145 R 10C 145 R 12C 145 R 13C 145 R 14C 145 R 15C 155 R 12C 155 R 13C 155 R 14C 165 R 13C 165 R 14C 165 R 15C 175 R 13C 175 R 14C 175 R 16C 185 R 13C 185 R 14C 185 R 15C 185 R 16C 195 R 14C 195 R 15C 195 R 16C 205 R 14C 205 R 15C 205 R 16C 215 R 14C 215 R 15C 215 R 16C 245 R 16C 17 R 15C 17 R 380C 17 R 400C 19 R 400C | 4.00 4.00 4.00 4.00 4.00 4.50 4.50 4.50 4.50 4.50 4.50 5.00 5.00 5.00 5.50 5.50 5.50 5.50 5.50 5.50 5.50 6.00 6.00 6.00 6.00 6.00 6.00 7.00 5.00 5.00 150mm 150mm | 254 305 330 356 381 305 330 356 330 356 381 330 356 406 330 356 381 406 356 381 406 356 381 406 356 381 406 406 381 381 400 400 | 492 542 566 590 616 550 578 604 596 622 646 608 634 684 624 650 674 700 666 690 716 686 710 736 700 724 750 798 678 678 678 728 | - - - - - - - - - - - - - - - - - - - - - - - - - - - 798 - - - - | 147 147 147 147 147 157 157 157 167 167 167 178 178 178 188 188 188 188 198 198 198 208 208 208 218 218 218 248 178 178 186 200 | - - - - - - - - - - - - - - - - - - - - - - - - - - - 248 - - - - |
| Code Designated |
| 5.60 R 12C 6.40 R 13C 6.70 R 13C 6.70 R 14C 6.70 R 15C | 4.00 5.00 5.00 5.00 5.00 | 305 330 330 356 381 | 570 648 660 688 712 | 572 640 662 688 714 | 150 172 180 180 180 | 148 172 180 180 180 |

Note: (+)Tyres in diagonal construction are identified by an hyphen in place of the letter 'R' (e.g. 145-10 C).

        - Tyres for special applications-Radial and diagonal construction

| Tyre size designation | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm) | Section width S (mm) |
| --- | --- | --- | --- | --- |
| Code Designated |
| 15x4 1/2-8 16x6-8 18x7 18x7-8 21x8-9 21x4 22x4 1/2 23x5 23x9-10 25x6 27x10-12 28x9-15 | 3.25 4.33 4.33 4.33 6.00 2.32 3.11 3.75 6.50 3.75 8.00 7.00 | 203 203 203 203 229 330 330 330 254 330 305 381 | 385 425 462 462 535 565 595 635 595 680 690 707 | 122 152 173 173 200 113 132 155 225 170 255 216 |
| Metric designated |
| 200-15 250-15 300-15 | 6.50 7.50 8.00 | 381 381 381 | 730 735 840 | 205 250 300 |

Note: (+)Tyres in radial construction are identified by the letter 'R' in place of the hyphen '-' (e.g. 15x4 1/2 R 8).

        - Tyres for light commercial vehicles (LT Tyres) diagonal and radial

| Tyre size designation1 | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm)2 | Section width S (mm)3 |
| --- | --- | --- | --- | --- |
|  |  |  | Normal | Snow |  |
| 6.00-16LT 6.50-16LT 6.70-16LT 7.00-13LT 7.00-14LT 7.00-15LT 7.00-16LT 7.10-15LT 7.50-15LT 7.50-16LT 8.25-16LT 9.00-16LT G78-15LT H78-15LT L78-15LT L78-16LT 7-14.5LT4 8-14.5LT4 9-14.5LT4 7-17.5LT 8-17.5LT | 4.50 4.50 5.00 5.00 5.00 5.50 5.50 5.00 6.00 6.00 6.50 6.50 6.00 6.00 6.50 6.50 6.00 6.00 7.00 5.25 5.25 | 406 406 406 330 356 381 406 381 381 406 406 406 381 381 381 406 368 368 368 445 445 | 732 755 722 647 670 752 778 738 782 808 859 890 711 727 749 775 677 707 711 758 788 | 743 767 733 658 681 763 788 749 794 819 869 903 722 739 760 786 769 799 | 173 182 191 187 187 202 202 199 220 220 241 257 212 222 236 236 185 203 241 189 199 |

Note: 1/Tyres in Radial construction are identified by the letter "R" in place of "-" (e.g. 6.00 R 16LT).

2/Coefficient "b" for the calculation of Dmax: 1.08.

3/Overall width may exceed this value up to +8 per cent.

4/The suffix "MH"' may replace "LT" in the tyre size designation (e.g. 7-14.5 MH).

        - Tyres for light commercial vehicles (High flotation tyres) diagonal and radial

| Tyre size designation1 | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm)2 | Section width S (mm)3 |
| --- | --- | --- | --- | --- |
|  |  |  | Normal | Snow |  |
| 9-15LT 10-15LT 11-15LT 24x7.50-13LT 27x8.50-14LT 28x8.50-15LT 29x9.50-15LT 30x9.50-15LT 31x10.50-15LT 31x11.50-15LT 31x13.50-15LT 31x15.50-15LT 32x11.50-15LT 33x12.50-15LT 35x12.50-15LT 37x12.50-15LT 37x14.50-15LT 8.00-16.5LT 8.75-16.5LT 9.50-16.5LT 10-16.5LT 12-16.5LT 30x9.50-16.5LT 31x10.50-16.5LT 33x12.50-16.5LT 37x12.50-16.5LT 37x14.50-16.5LT 33x9.50 R15LT 35x12.50 R16.5LT 37x12.50 R17LT | 8.00 8.00 8.00 6 7 7 7.5 7.5 8.5 9 11 12 9 10 10 10 12 6.00 6.75 6.75 8.25 9.75 7.50 8.25 9.75 9.75 11.25 7.50 10.00 10.00 | 381 381 381 330 356 381 381 381 381 381 381 381 381 381 381 381 381 419 419 419 419 419 419 419 419 419 419 381 419 432 | 744 773 777 597 674 699 724 750 775 775 775 775 801 826 877 928 928 720 748 776 762 818 750 775 826 928 928 826 877 928 | 755 783 788 604 680 705 731 756 781 781 781 781 807 832 883 934 934 730 759 787 773 831 761 787 838 939 939 832 883 934 | 254 264 279 191 218 218 240 240 268 290 345 390 290 318 318 318 372 203 222 241 264 307 240 266 315 315 365 240 318 318 |

Note: 1/Tyres in Radial construction are identified by the letter "R" in place of "-" (e.g. 24x7.50 R 13LT).

2/Coefficient 'b' for the calculation of Dmax: 1.07.

3/Overall width may exceed this value up to +7 per cent.

        - Code designated tyres mounted on 5 degrees tapered or flat base rims diagonal and radial

| Tyre size designation1 | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm)2 | Section width S (mm)3 |
| --- | --- | --- | --- | --- |
|  |  |  | (a) | (b) | Snow |  |
| 6.50-20 7.00-15TR 7.00-18 7.00-20 7.50-15TR 7.50-17 7.50-18 7.50-20 8.25-15TR 8.25-20 9.00-15TR 9.00-20 10.00-15TR 10.00-20 10.00-22 11.00-20 11.00-22 11.00-24 11.50-20 12.00-20 12.00-24 14.00-20 14.00-24 | 5 5.5 5.5 5.5 6 6 6 6 6.5 6.5 7 7 7.5 7.5 7.5 8 8 8 8 8.5 8.5 10 10 | 508 381 457 508 381 432 457 508 381 508 381 508 381 508 559 508 559 610 508 508 610 508 610 | 878 777 853 904 808 859 884 935 847 974 891 1019 927 1054 1104 1085 1135 1186 1085 1125 1226 1241 1343 | 855 982 904 1031 940 1067 1118 1099 1150 1201 1099 | 893 792 868 919 825 876 901 952 865 992 911 1038 946 1073 1123 1104 1155 1206 1104 1146 1247 1266 1368 | 184 199 199 199 215 215 215 215 236 236 259 259 278 278 278 293 293 293 296 315 315 375 375 |

Note: 1/Tyres in Radial construction are identified by the letter "R" in place of "-".(e.g. 6.50 R 20).

2/Coefficient 'b' for the calculation of Dmax : 1.06.

3/Overall width may exceed this value up to +6 per cent.

        - Code designated tyres for special services diagonal and radial

| Tyre size designation | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm)1 | Section width S (mm)2 |
| --- | --- | --- | --- | --- |
|  |  |  | (a) | (b) |  |
| 10.00-20ML 11.00-22ML 13.00-24ML 14.00-20ML 14.00-24ML 15-19.5ML 24 R 21 | 7.5 8 9 10 10 11.75 18 | 508 559 610 508 610 495 533 | 1073 1155 1302 1266 1368 1019 1372 | 1099 1182 | 278 293 340 375 375 389 610 |

Note: 1/ Coefficient "b" for the calculation of Dmax : 1.06.

2/Overall width may exceed this value up to +8 per cent.

        - Code designated tyre mounted on 15 degrees tapered rims diagonal and radial

| Tyre size designation1 | Measuring rim width code | Nominal Diameter d (mm) | Outer Diameter D (mm)2 | Section width S (mm)3 |
| --- | --- | --- | --- | --- |
|  |  |  | (a) | (b) | Snow |  |
| 8-19.5 8-22.5 9-22.5 10-22.5 11-22.5 11-24.5 12-22.5 12-24.5 12.5-22.5 12.5-24.5 14-17.5 15-19.5 15-22.5 16.5-22.5 18-19.5 18-22.5 | 6.00 6.00 6.75 7.50 8.25 8.25 9.00 9.00 9.00 9.00 10.50 11.75 11.75 13.00 14.00 14.00 | 495 572 572 572 572 622 572 622 572 622 445 495 572 572 495 572 | 859 935 974 1019 1054 1104 1085 1135 1085 1135 907 1005 1082 1128 1080 1158 | 982 1031 1067 1118 1099 1150 1099 1150 | 876 952 992 1038 1073 1123 1104 1155 1104 1155 921 1019 1095 1144 1096 1172 | 203 203 229 254 279 279 300 300 302 302 349- 389- 389- 425- 457- 457- |

Note: 1/Tyres in Radial construction are identified by the letter "R" in place of "-" (e.g. 8R19.5).

2/Coefficient "b" for the calculation of Dmax : 1.05.

Category of use: Normal Service tyres: (a) Highway tread (b) Heavy tread

3/Overall width may exceed this value up to +6 per cent

(-)Overall width may exceed this value up to +5 per cent.

      - A conventional number denoting the nominal rim diameter and corresponding to its diameter expressed either by codes (numbers below 100) or in millimetres (numbers above 100)

      - The indication of the structure

    - Test method

      - Load/speed endurance test

        - Preparing the tyre

          - Mount a new tyre on the standard test rim.

          - Use a new inner tube or combination of inner tube, valve and flap (as required) when testing tyres with inner tubes.

          - Inflate the tyre to the pressure corresponding to the pressure index specified by the manufacturer

          - Condition the tyre-and-wheel assembly at test-room temperature for not less than three hours.

          - Readjust the tyre pressure to that specified in paragraph 28.5.3.1.1.3 above.

        - Test procedure

          - Mount the tyre-and-wheel assembly on the test axle and press it against the outer face of a smooth power-driven test drum 1.70 m +/- 1% in diameter having a surface at least as wide as the tyre tread.

          - Apply to the test axle a series of test loads expressed in percent of the load indicated opposite the load index engraved on the sidewall of the tyre. Where the tyre has load-capacity indices for both single and twinned utilization, the reference load for single utilization shall be taken as the basis for the test loads.

            - In the case of a tyre with a load capacity index 121 or less and a speed category above P test procedures are as specified in paragraph 28.5.3.1.3.

            - For all other tyre types the endurance test programme is shown as follows:

| Load index | Tyre speed category | Test-drum speed | Load placed on the wheel as a percentage of the load corresponding to the load index |
| --- | --- | --- | --- |
|  |  | Radial-ply min-1 | Diagonal(bias-ply) min-1 | 7h | 16h | 24h |
| ≧122 | F G J K L M | 100 125 150 175 200 225 | 100 100 125 150 - - | 66% | 84% | 101% |
| <=121 | F G J K | 100 125 150 175 | 100 125 150 175 |  |  |  |
|  | L | 200 | 175 | 70% | 88% | 106% |
|  |  |  |  | 4h | 6h |  |
|  | M N P | 250 275 300 | 200 - | 75% 75% 75% | 97% 97% 97% | 114% 114% 114% |

Notes:

(1) "Special-use" tyres should be tested at a speed equal to 85% of the speed prescribed for equivalent normal tyres.

(2) Tyres with load index 121 or more, speed categories N or P and the additional marking "LT" included in the tyre size designation, shall be tested with the same programme as specified in the above table for tyres with load index 121 or less.

          - The tyre pressure must not be adjusted throughout the test and the test load must be kept constant.

          - During the test the temperature in the test-room must be maintained at between 20 ℃ and 30 ℃ or at a higher temperature if the manufacturer so agrees.

          - The endurance-test programme shall be carried out without interruption.

        - Load/speed test programme for tyre with a load capacity index 121 and less, or the additional marking "LT" included in the tyre size designation, and a load capacity index above 121 and a speed category Q and above

          - Load placed on the wheel as a percentage of the load corresponding to the load index:

            - 90% when tested on a test drum 1.70 m +/- 1% in diameter.

            - 92% when tested on a test drum 2.0 m +/- 1% in diameter.

          - Initial test speed: speed corresponding to the speed category symbol less 20 km/h;

Time to reach the initial test speed 10 min.

Duration of the first step = 10 min.

          - Second test speed: speed corresponding to the speed category symbol less 10 km/h; Duration of the second step = 10 min.

          - Final test speed: speed corresponding to the speed category symbol; Duration of the final step = 30 min.

          - Total test duration: 1 h.

        - If a method other than that described in paragraph 28.5.3.1.2 above is used, its equivalence must be demonstrated.

    - Requirements

      - Load/speed endurance test

        - Each type of pneumatic tyre shall undergo at least one load/speed endurance test.

        - A tyre which, after undergoing the endurance test, does not exhibit any tread separation, ply separation, cord separation, chunking or broken cords shall be deemed to have passed the test.