- The electronic control device of small-light moped

  - From 2007/06/01 , a small-light moped’s electronic control device have to comply with this Regulation.

  - The electronic control device of small-light moped shall according to suitable variants and range of principle are as below：

    - The same vehicle category symbol.

    - The same brand and vehicle type.

  - The small-light moped’s maximum speed rate shall be under 45 km per hour.

  - The small-light moped’s electronic control device have to comply with following requirements:

    - The voltage of battery: a battery’s announced voltage is equal to 48 volt or less than 48 volt.（Test data is permit promoting 20 percent of voltage. ）

    - Motor power: The most output power of motor is equal to 1.34 horsepower or less than 1.34 horsepower（1000 watt）.

    - Exceeded the speed limit of electronic disconnection: if speed is exceed 45 km per hour, motors should disconnect electronic within 3

seconds.

    - Breakdown of electronic disconnection: if exceeded signal’s input line is short circuit or broken circuit of control system, the motor should

disconnect electronic within 3 seconds.