- The frame’s fatigue strength of small-light moped

  - From 2007/07/01, the fatigue strength of the frame of small-light moped shall comply with this Regulation.

  - The frame’s fatigue strength of small-light moped shall according to suitable variants and range of principle are as below：

    - The same vehicle category symbol.

    - The same brand and vehicle type.

  - Testing methods:

    - Each seat tube’s load is 50 kilograms.

    - The head tube’s load is 5 kilograms on two sides of handlebar.

    - The load of the foot step plane is 20 kilograms.

    - Testing frequency is upward 6.6 Hz, and below 10 Hz.

    - Acceleration is 19.6 m/sec2（2G）.

    - The cycles of vibration is seventy thousand.

  - Testing standard: there is no breakage of the frame of moped is after the test.